## Slide 1
College of Engineering,
Electrical Engineering Department
Arithmetic Operation
By:
Asst Lec. Besma Nazar Nadhem
Class : Second Year
Subject : Digital Techniques
Master of Science in Electrical Engineering
(Electronic and Communication)

## Slide 2
Arithmetic operations
Basic arithmetic operations include addition, subtraction, multiplication and division .
Basic Rules of Addition:
Binary Addition:
the basic rules of binary addition as follows:
1. 0 + 0 = 0.
2. 0 + 1 = 1.
3. 1 + 0 = 1.
4. 1 + 1 = 0 with a carry of ‘1’ to the next more significant bit.
5. 1 + 1 + 1 = 1 with a carry of ‘1’ to the next more significant bit.

## Slide 3
Example: Add the following binary number:
a)11+11 b)11+111
Solution:
a) 11 b)011
11+ 111 +
110 1010
2. Octal Addition:
If the sum result >= 8 , subtract 8 and carry 1
Example: Add the following octal number:
57+432
057
432+
511

## Slide 4
3. Hexadecimal Addition:
If the sum result >= 16 , subtract 16 and carry 1
Example: Add the following Hexadecimal number:
58+4B
58
4B+
A3
Complement :
Complement are used in digital computer for simplifying the subtraction operation and for logical manipulation. There are two types of complement for each base system the r’s and (r-1)’ complement.

## Slide 5
Binary Number Complement
In binary number system we have the 1’s and 2’s complement the 1’s is obtained by replacing 0s with 1s and 1s with 0s.
2’s complement = 1’s complement +1.
Example : Find the 1’s and 2’s complement of the following number : 1011000.
Solution :
1’s comp.=0100111 ;2’s =0100111+1=0101000
2. Decimal Number Complement
In decimal number system we have the 9’s and 10’s complement the 9’s is obtained by subtracting each digit from 9
10’s complement = 9’s complement +1.

## Slide 6
Example : Find the 9’s and 10’s complement of the following number :2496.
Solution :
9’s comp.= 9999-2496 = 7503;10’s =7503+1=7504
3. Octal Number Complement:
In octal number system we have the 7’s and 8’s complement the 7’s is obtained by subtracting each digit from 7
8’s complement = 7’s complement +1.
Example : Find the 7’s and 8’s complement of the following number :562.
Solution :
7’s comp.= 777- 562 = 215;8’s =215+1=216

## Slide 7
4. Hexadecimal Number Complement:
In hexadecimal number system we have the 15’s and 16’s complement the 15’s is obtained by subtracting each digit from 15
16’s complement = 15’s complement +1.
Example : Find the 15’s and 16’s complement of the following number :3BF.
Solution :
15’s comp.= 15 15 15 – 3 B F = C 4 0;16’s =C 4 0+1=C 4 1

## Slide 8
Subtraction with Complements
The efficient method for subtraction is used complement . The subtraction of two n-digit numbers M-N can be :
1- If use (r-1)’s complement [1’s 9’s 7’s 15’s]:
If the sum produce an end carry which can be added to the sum.
If the sum does not produce an end carry take the (r-1)’s comp. of the sum and place – sign.
2- If use (r)’s complement [2’s 10’s 8’s 16’s]:
If the sum produce an end carry which can be discarded.
If the sum does not produce an end carry take the (r)’s comp. of the sum and place – sign.

## Slide 9
Example : Subtract the following binary number :
1010100-1000011 b)1000011-1010100
Solution :
1)Using 1’s comp. 2)Using 2’s comp.
a)1010100 b)1000011 a)1010100 b) 1000011
1000011- 1010100- 1000011- 1010100-
1010100 1000011 1010100 1000011
0111100+ 0101011+ 0111101+ 0101100+
10010000 1101110 10010000 1101111
1+ 1’s=0010001 2’s=0010001
0010001 -(0010001) discarded -(0010001)

## Slide 10
Example : Subtract the following decimal number : 72532-3250
Solution:
1)Using 9’s comp. 2)Using 10’s comp.
72532 72532
03250- 03250-
72532 72532
96749+ 96750
169281 169282
1+
69282
Example : Subtract the following octal number : 256-341
Solution :
1)Using 7’s comp. 2)Using 8’s comp.
256 256
341- 341-
256 256
436 437
discarded

## Slide 11
715
7’s comp. =063 8’s comp.= 063
-(63) –(63)
Example : Subtract the following hexadecimal number : 592-3A5
Solution :
1)Using 15’s comp. 2) Using 16’s comp.
592 592
3A5 3A5
592 592
C5A C5B
11EC 11ED
1+
1ED
discarded