## Slide 1: Transportation Engineering
Civil Engineering Department
4th Stage, 1st Semester, 2019-2020
Traffic Characteristics, Examples on Traffic volume
Lecturer
Dr Abeer K.Jameel, Dr Maha Osamah

## Slide 2: Traffic Characteristics: Examples
Question
Traffic volume data has been collected for 15 min time intervals as shown below.
Find the total hourly volume, flow rate and peak hour factor (PHF).
Time | 7:30-7:45 | 7:45-8:00 | 8:00-8:15 | 8:15-8:30
Volume | 250 | 350 | 300 | 200

## Slide 3: Traffic Characteristics: Examples
Solution
Total hourly volume= 250+350+300+200 = 1100 veh
Number of intervals =4
Peak interval …> 7:45-8:00
Peak volume per interval 350 v/15min.
Flow rate= Peak interval volume *number of intervals
= 350*4=1400vph
PHF= total hourly volume/flow rate= 1100/1400= 0.786
Time | 7:30-7:45 | 7:45-8:00 | 8:00-8:15 | 8:15-8:30 | Total (Vph)
Volume | 250 | 350 | 300 | 200 | 1100

## Slide 4: Traffic Characteristics: Examples
Question
Traffic volume data has been collected for 10 min time intervals as shown below.
Find the total hourly volume, flow rate and PHF.
Time | 7:30-7:40 | 7:40-7:50 | 7:50-8:00 | 8:00-8:10 | 8:10-8:20 | 8:20-8:30
Volume | 150 | 200 | 300 | 200 | 150 | 100

## Slide 5: Traffic Characteristics: Examples
Solution
Total hourly Volume = 150+200+300+200+150+100=1100veh
Number of intervals =6
Peak interval …> 7:50-8:00
Peak volume per interval 300 v/10min.
Flow rate= Peak interval volume *number of intervals
= 300*6=1800vph
PHF= total hourly volume/flow rate= 1100/1800= 0.61
Time | 7:30-7:40 | 7:40-7:50 | 7:50-8:00 | 8:00-8:10 | 8:10-8:20 | 8:20-8:30 | Total
Volume | 150 | 200 | 300 | 200 | 150 | 100 | 1100

## Slide 6: Traffic Characteristics: Examples
Question
The daily counts of the current traffic volume for a rural highway and for both directions, for one week of May 2000, are as follows:
The traffic composition is 70% passenger cars, 20% buses and 10% trucks. The traffic is expected to be 180% from the current traffic up to May 2020. Find the required number of lanes for the highway if the lane capacity is 1300 pc/hr/ln. Assume k=0.15 and D=0.6
Day | Sat. | Sun. | Mon. | Tue. | Wed. | Thur. | Fri.
Daily Volume | 12000 | 12500 | 10500 | 11500 | 9500 | 9000 | 8500

## Slide 7: Traffic Characteristics: Examples
Solution
ADT=sum of traffic/Number of days
Current ADT=(12000+12500+10500+11500+9500+9000+8500)/7
= 10500 veh/day/2directions
Future ADT=10500*1.8=18900 veh/day/2directions.
DHV=ADT* K
=18900*0.15=2835 veh/hr/2directions
DDHV=DHV*D
=2835*0.6=1701 veh/hr/direction
DDHV (pcu/hr)=1701*0.7*1 +1701*(0.3)*1.5=1956 pcu/hr/ direc.
No. of lanes = 1956/1300 = 1.5 lanes (use 2 lanes)
…>4lanes/both direction