## Slide 1
5-4 SYSTEM MEMORY
Memory refers to the computer chips that store information for quick retrieval by the CPU. They are basically divided into two
ROM and RAM.

## Slide 2: 5-4-1 Random Access Memory (RAM):
Is used to store information and instructions that operate the computer’s programs.
Typically, programs are transferred from storage on a disk drive to RAM.
RAM is also known as volatile memory because the information within the computer chips is lost when power to the computer is turned off or the computer hanged.

## Slide 3: 5-4-2 Read-Only Memory (ROM)
Contains critical information and software that must be permanently available for computer operation, such as the operating system that directs the computer’s actions from start up to shut down.
ROM is called non-volatile memory because the memory chips do not lose their information when power to the computer is turned off.

## Slide 4: 5-5 HARDWARE CONNECTIONS
To function, hardware requires physical connections that allow components to communicate and interact.
A bus provides a common interconnected system composed of a group of wires or circuitry that coordinates and moves information between the internal parts of a computer.
A bus is characterized by two features:
How much information it can manipulate at one time, called the bus width, and how quickly it can transfer these data.

## Slide 5
1-A serial connection:
Is a wire or set of wires used to transfer information from the CPU to an external device such as a mouse, keyboard, modem, scanner, and some types of printers. This type of connection transfers only one piece of data at a time, and is therefore slow.
The advantage of using a serial connection is that it provides effective connections over long distances.

## Slide 6
2-A parallel connection:
Uses multiple sets of wires to transfer blocks of information simultaneously.
Most scanners and printers use this type of connection.
A parallel connection is much faster than a serial connection, but it is limited to distances of less than 3 m (10 ft) between the CPU and the external device.

## Slide 7: 5-6 COMPUTER SOFTWARE
Software is the set of instruction that tells the computer what to do and when to do it.
The computer uses this instruction to manipulate data, and enhance the proper functioning of the hardware components.
It is designed to exploit and provide the potential capabilities of the hardware to the user.
It converts data into information and allows users to use the computer in different ways.

## Slide 8
These programs are usually stored and transferred via the computer’s hardware to and from the CPU.
Software also governs how the hardware is utilized; for example, how information is retrieved from a storage device.
The interaction between the input and output devices is controlled by software called the Basic Input Output System (BIOS) Software.
Software as a whole can be divided into a number of categories based on the types of work done by programs.
The two primary software categories are system software, and application software.