## Slide 1: Environmental Health

## Slide 2
Environmental health relates to the impact the environment can have on a population. The environment refers to both the natural and human created environment.

## Slide 3
The NATURAL environment on its own may create problems for human health as evidenced by temperature fluctuations and such natural events as forest fires. For example, a heat wave may result in cases of forest fires will produce smoke resulting in respiratory problems.

## Slide 4
The CREATED environment also poses many risks to the health. For example, the slum areas of many cities are in themselves a health hazard, due to poor housing & poor availability of water & sanitation.

## Slide 5: Environment
Aggregation of all external conditions & influences that affect the life & development of any living subjects as well as affect human behavior & society.

## Slide 6
TYPES OF ENVIRONMENT

## Slide 7: Physical Environment
Geographical factors:
affect either – directly → through location
Geological factors:
which decide – Occupation e.g. agriculture.
– Industry e.g. mining.
– Type of water, mineral, deposits.

## Slide 8: Physical Environment Cont.
Climatic factors:
(temperature, humidity, air movement)
affect on – Habit of people “Host”.
– Pathogen vectors.
– Seasonal fluctuation.

## Slide 9: Biological Environment
Universe of living things surround man
- animals
- plants
Whether acting as agent, reservoir, or vector or otherwise important in concern with
- Communicable disease - agent
- vector
-reservoir
- Relation to food supply - plant origin
- animal origin

## Slide 10: Sociocultural Environment
Affects through: →
    Population density.
    Education state.
    Medical care facilities.
    Mean of transportation.

## Slide 11: Economic Environment
 Factors related to economic status:
e.g. Poverty lead to:
 Malnutrition.
 Bad sanitation.
 Bad housing.

## Slide 12: Important NOTES in assessment of Environmental Problems
The problem may arise from multiple factors which enter the body by different routes.
The agent that were originally not toxic to the people may become so & vice versa “by the process of transportation & degradation”.
Once the level of exposure is known, it can be compared with existence stander.

## Slide 13: Current Environmental Situation
Air pollution.
Unsafe water supply.
Excreta Disposal
Industrial waste collection & disposal.
Green house effect “global warming”.
Ozone layer destruction.
Acidic deposition.

## Slide 14
Environmental health addresses all the physical, chemical, and biological factors external to a person, and all the related factors impacting behaviors. It encompasses the assessment and control of those environmental factors that can potentially affect health.

## Slide 15
Air pollution:
Definition:
The presence in the atmosphere of one or more air contaminants in such quantities that are harmful to human, plant, or animal life, or that interfere with the comfortable enjoyment of life or the conduct of business or other human activities

## Slide 16
Clean air is considered to be a basic requirement of human health and well-being. However, air pollution continues to pose a significant threat to health worldwide.

## Slide 17
According to a WHO assessment, more than 2 million premature deaths each year can be attributed to the effects of air pollution. More than half of this disease burden is borne by the populations of developing countries.

## Slide 18
Constituents of air:
Nitrogen 78%,
Oxygen 21%,
CO2 0.03%,
Argon, neon, helium, crypton & xenon <1%

## Slide 19
Factors contributing to air pollution;
1-Industrialization
2-Sharp increase in population
3-Urbanization
4-Mobility
5-Consumption of products

## Slide 20
Sources of pollutants
(Mobile, stationary);
Mobile sources; e.g. cars, trucks, buses, motorcycles, boats, and planes contributes to more than half of air pollution in USA. The exhaust from these sources includes; CO, volatile organic compounds (VOCs), nitrogen oxides (NOx), particulates and lead.
Notes: <number>

## Slide 21
Stationary sources;
e.g. iron and steel plants, oil refineries, dry cleaner, and gas stations. The electric utilities, factories and commercial buildings burn coal, oil, natural gas, wood, and other fuels, so are the principle sources of SO2, NOx, CO, particulates, VOCs, and lead.

## Slide 22
Criteria pollutants:
They are of great threat to air quality. They include ozone, CO, particulates, SO2, NOx, Hydrocarbons, and lead.

## Slide 23
Hazardous pollutants:
They could contribute to an increase in
mortality and serious illness, e.g. asbestos, beryllium, mercury, vinyl chloride, arsenic, benzene.

## Slide 24
Sources of air pollution:
1-Natural sources:
e.g. Fog, dust, gases from fissures and cracks in the earth, volcanoes producing ash, gas, fumes, and smoke, from forest fires, pollens from plants and weeds.
Effects: The most important is pollen. it produce hay fever and allergies.

## Slide 25
2-External combustion:
Takes place in furnaces and boilers. The furnace is a combustion chamber in which air and fuel are mixed and heat is applied to release large quantities of stored energy from the fuel.
Incomplete combustion results from too much or to little air, too low temperature, and inadequate time allowed for the burning process.

## Slide 26
3-Internal combustion:
Inadequate quantities of air in the combustion process results in emission of CO instead of CO2, unburned gasoline and a variety of hydrocarbons.
The extremely hot air in the engine converts the nitrogen and oxygen of the air into the nitrogen oxide that helps produce photochemical smog.

## Slide 27
4-Attrition:
Attrition is wearing or grinding down by friction. Attrition occurs from the process of grinding, spraying, demolishing or from simply walking or driving.
In any situation where friction is present, some portion of the surface in contact will break off in minute particles into the atmosphere.

## Slide 28
5-Evaporation:
“Change of state of liquid into a gas at any temperature below its boiling point”. Odor type pollution will result e.g. emission of organic solvents from dry cleaning plants.

## Slide 29
6-Incineration:
Solid waste garbage, refuse, sludge, and other discarded solid materials.
These are both combustible and non-combustable. They result from industrial, commercial, agricultural, and community activities.

## Slide 30
6-Incineration:
Incinerations are used to reduce the volume of these materials.
The inefficient incinerators emit fly ash, smoke, gases, and odors.
Open burning causes the emission of particulates, CO, HC, SOx, and odor.

## Slide 31
7-Specific sources:
Depends on type of industry in the area;
  Petroleum refineries: Emit HC, hydrogen sulfide, waste gases, smoke, CO, Nox , SO2, and other odorous gases.

## Slide 32
7-Specific sources:
  Power plants: They generate electricity by burning coal, and oil that may contain sulfur as an impurity. The emission from power plants include; CO, CO2, NOx, HC, and particulate matters

## Slide 33
The impact of air pollution of the body:
Human exposure to air pollution can be estimated by determining the concentration of hazardous air pollutants
by use of;
1-Personal samplers.
2-Blood samplers.

## Slide 34
Factors to be considered when determining human exposure;
-What and how much is emitted?
-Seasonal and weather conditions.
-How much a person inhales?
-Personal susceptibility.

## Slide 35
Humans are exposed to a large number of physical or chemical genotoxic agents, some of which take years to induce disease. These agents may act alone or synergistically. These agents may be mutagenic, carcinogenic or both.

## Slide 36
Once the particulates and bound chemical enter the respiratory tract, they may become metabolized. Metabolism may result in products that are relatively nontoxic and cleared rapidly form the body, or the chemicals may be metabolized to a more chemically reactive species capable of reacting with cellular macromolecules such as DNA.

## Slide 37
Effects on respiratory system:
1-Slowing down or stopping the action of cilia. The function of cilia is to sweep the mucus loaded with microorganism and dirt out of the respiratory tract.
2-Increasing or thickening of the mucus.
3-Constriction of air passages.
4-Breathing may become more difficult because of mechanical blockage or because of an ineffective exchange of O2 and OC2 in the alveoli.

## Slide 38
Effects on the eye:
The conjunctiva and cornea will be affected (because they are in direct contact with the atmosphere). Therefore eye irritation occurs.
The resultant tears are a mechanism to flush the foreign material from the eyes.
Photochemical air pollution causes eye irritation and decreased visibility.

## Slide 39
Systemic effect:
Damage to blood cells, liver, kidneys, and nervous system.

## Slide 40
Economic effects:
1-Effects on animals:
-Affected by breathing and ingestion of grass contaminated by the residues of the various pollutants. e.g. animals grazing within the vicinity of a lead foundry, may become sick and die due to lead poisoning.
- Less egg production (chickens), thinner coat of wool (sheep), and less milk (cows).

## Slide 41
2-Effects on vegetations:
-Crops are destroyed.
- Ornamental plants become spotted نباتات الزينة and late destroyed.
e.g. plant pollutants; SO2, hydrogen fluoride, photochemical smog, and HC.

## Slide 42
3-Effects on materials:
-Abrasion by particulate pollutants.
-Discoloration of materials form grey-brown to black by hydrogen sulfide.
Paints are faded by oxides of nitrogen, -SO2.
-Cracking of tires because of smog.

## Slide 43
4-Effects on visibility:
-Impaired visibility is due to the scattering of sunlight by particulates suspended in the atmosphere. NO2 is also a problem because it is a yellow-brown gas, which in substantial concentration reduces light.

## Slide 44
Costs due to air pollution (The economic burden of air pollution on the society);
-Higher medical costs due to sickness and accidents.
-Loss of livestock.
-Increased maintenance.
-Higher cleaning bills.
-Greater absenteeism.
-Reduced or destroyed crops.
Notes: <number>

## Slide 45
Greenhouse effect:
Atmospheric gases in the troposphere stabilize the earth’s temperature. These gases permit the passage of visible and UV radiation from the sun, which warms the earth’s surface, but blocks the escape back into space of reflected infrared radiation.

## Slide 46
Greenhouse effect:
Without these gases, the earth’s temperature will be less than zero. But if the concentration of these gases rises, this will lead to an increase in the temperature of the biosphere.

## Slide 47
The responsible gases are:
CO, NOx, Methane, Chlorofluorocarbons (CFCs), ozone.
Sources of these gases:
-Internal combustion engines.
-Coal-burning electric power generators.
-Various industrial processes.

## Slide 48
Effect of global temperature:
The global temperature increased by 0.5 – 1 C from the year 1880 – 1990. If the problem continues the global temperature will rise by 3 – 4 C in the next 50 – 100 years. This will affect;
-Local, regional, and global ecosystems.
-Sea levels and ocean currents.
-Prevailing winds.
-Agriculture.

## Slide 49
-Forests.
-Industry.
-Transport.
-Human health; Potential health effects which may occur as a result of the increased temperature; Sunburn  cancer; cataract; immune system effects; respiratory effects; heat stress; vector born diseases; malnourishment due to reduced food supply

## Slide 50
Ozone depletion:
The stratospheric ozone layer (which is located 12 – 24 kilometer far from earth’s surface) is very important because it protects people from the harmful biological effects of UVB (290 – 320 nm) which may cause DNA damage.

## Slide 51
Chemicals accused to destroy ozone are:
-Oxides of nitrogen emitted as exhaust gases by high-flying supersonic jet aircrafts.
-CFCs used as propellants in spray cans, refrigerators and solvents.

## Slide 52
Size of the problem:
The stratospheric ozone layer was found to be thinning over Antarctica in 1984 – 1985 by about one third.
In 1990, the attenuation of the Southern hemisphere involved southern Australia and Argentina.

## Slide 53
Size of the problem:
Attenuation has also been observed in the Northern hemisphere.
Note: Stratospheric ozone depletion must not be confused with tropospheric ozone accumulation (one of the greenhouse gases).

## Slide 54
Adverse effects:
1-Effects on the skin.
-Sunburn (simple erythema to severe blistering).
-Solar elastosis (brown, dry, wrinkled skin condition)
A 2% decrease in stratospheric ozone produces a 4% increase in non-melanoma skin cancer (basal cell and squamous skin cancer).

## Slide 55
Adverse effects:
2-Effects on the eye: UVB radiation causes
aging of the eye lenses. it may cause cataract.
3-Depression of the immune system.

## Slide 56
4-Increase in temperature:
-Increased temperature at ground level tends to increase ozone pollution, which can irritate and inflame the respiratory tract.
-Heat stress, although a minor problem for healthy individuals may become very serious for the very young, the very old people with heart or respiratory problems.

## Slide 57
4-Increase in temperature:
-Vector born diseases increase with higher temperature and more rain. Since insects become more prevalent, there is greater possibility of disease if the organisms which cause disease are present in the insects.
-Food supply may decrease with increasing temperature. Higher yields of food are found in temperate or colder climates.

## Slide 58
Air pollution control:
1-Isolation : Separation of heavy industry by distance from cities (industrial plants in rural area).
2-Shielding. e.g. placing asthmatics in air-conditioned quarters (not feasible).
3-Legislation: With continuous monitoring of community air to determine its quality in comparison with the standards.

## Slide 59
4-Substitution:
-Use of sanitary landfills avoids air pollution form either burning dumps or incineration.
-Use of lower sulfur fuel, so decrease SO2.
-Burning nature gases  Less pollution .
-Generation of electricity by use of atomic fuel avoids most air pollution problems associated with fossil fuels.

## Slide 60
4-Substitution:
-source pollution control: Accompanied by preventing the pollutant from forming through changing existing industrial operations through developing equipment that destroys, alter or traps the pollutant.

## Slide 61
Air pollution control programs:
-Need cooperation between local and governmental agencies, industry and the population.
-A good program must include legal authority to institute and carry out an air pollution control program.
-A continuing air quality monitoring program.

## Slide 62
-Development of air quality goals and standards based on air quality criteria.
-Health education program
-Identifying polluting industries and use of force when needed to achieve compliance