## Slide 1: What is Lead?
Lead is a blush gray metallic element which occurs naturally (in small amounts) in the earth’s crust.
It is dense, hence its use as a ballast, ammunition, or radiation shield.
Lead is insoluble in water, but some salts are soluble.
Notes: What is lead? And what are its characteristics?
Lead is a blue-gray, heavy, soft metallic element that occurs naturally in the earth’s crust. It is a malleable metal, so it can be easily worked - you can hammer it into protective sheets or make pipes and bend them easily. It is dense, and has good shielding protection against radiation, so it is used as ballast or to shield against penetrating forms of ionizing radiation. Metallic lead is tasteless and odorless, although some of the oxides and salts of lead taste sweet. (This sweet taste of lead salts is a source of problems for children!). Lead is insoluble in water, but some of the salts do dissolve, hence lead salts can be carried long distances in water supplies. Lead fumes will be easily formed when lead is heated. Although there is not a lot of lead in the earth’s crust – lead is ubiquitous, especially in modern industry.

## Slide 2: Lead- It’s Everywhere
USES OF Pb
Storage batteries Automobile radiators
Cable coating Brass and bronze Production
Radiation shielding Construction
Ammunition Printing
Plating insecticides
Paint Plastics
Soldering Television electronics
Petroleum Insecticides
Notes: Despite policy advances, how do we still get exposed to lead?
Lead exposure comes from new products or from lead already distributed into the human environment. Lead remains a component of many useful products. Examples include batteries, circuitry, medical shielding devices, gasoline (in some developing countries), cans and ceramic glazes (again, when regulatory control is poor), cable coatings (for example, as a “plasticizer” in the plastic coating your phone line), some types of printing, brass and bronze manufacture, galvanized metals and metal plating, solder (for example in plumbing) some ceramics, and even insecticides. Lead is also used extensively in ammunition, in both the explosive (lead stearate) and to add weight to the bullet. Workers engaged in the manufacture, use, reclamation, or recycling of any of these common products may be lead poisoned. Children may become exposed when parents purchase products, or when parents bring home contaminated articles from work, for example - lead dust on their clothes or in their car.

## Slide 3
Unusual oral sources of lead:
Ceramic vases,
art pottery,
Lead crystal glass used to contain fruit and alcohol products,
certain cosmetics applied to hands or face, folk medicines.
Notes: Slide 13. Unusual Oral Sources of Lead
There are some distinctly unusual sources of oral exposure to lead that are worth mentioning. Historically, “moonshine” whisky made in lead glazed vats or even radiator coils was a rich source of folklore and TV shows, as well as a source of lead poisoning.
Primitive evaporating equipment for concentrating maple syrup can be a source of lead. Glazed pottery from some developing countries should not be used for food. Ceramic vases are an important source of population lead poisoning internationally – in Mexico, for example. Art pottery belongs on the shelf, not in the kitchen. Lead crystal is expensive and beautiful, yet materials such as fruits and wines, sherries and other alcoholic beverages can leach some of the lead from the crystal. Folk remedies, and cosmetics of certain ethnic groups sometimes contain lead. So do “tin” solders. Lead has been found in the wicks of certain kinds of candles. Children have been poisoned by lead in pool cue chalk. There are many potential, unpredictable sources of lead. All of these unusual sources, together, are far less important in the U.S. than lead from paint and soils.

## Slide 4
What is Lead Paint?
Lead paint uses LEAD as a pigment.
It was advantageous to do this because it “sticks” (coats and penetrates into) well.
There are 2 types-
White lead (basic lead carbonate)
Red lead (a form of lead oxide)
Notes: What is Lead Paint (and why is lead in it)?
Lead improves paint both as a pigment and as a binder. Lead paint “sticks” (both penetrates into and coats the painted surface) very well. Furthermore, lead is a surface biocide, and protects against some kinds of microbial overgrowth. White lead is a basic lead carbonate; red lead is a form of lead oxide. These pigments may be used in many different color mixes. The color isn’t as important as the amount of lead present – up to 50% lead by weight. This is a lot of lead, and it is spread (as paint) over a large surface area, “perfect” for creating subsequent exposure.

## Slide 5: How does lead enter the body?
Respiratory
  Breathing in dust that contain lead. Lead is absorbed and distributed to other parts of the body via the bloodstream.
Notes: How Does Lead Enter the Body?
Lead is usually encountered by inhalation or oral ingestion. Respiratory exposure is more commonly the primary route in adults, while ingestion is often most important in children. Most cases of lead poisoning feature contributions of both inhalation and ingestion. Most of an inhaled lead dose is absorbed.

## Slide 6: How Does Lead Enter the Body?
2. Ingestion
Adults absorb about 6% of ingested lead. Fasting adults absorb more.
Children absorb much more lead
(30% if well fed, and more, 50% if fasting or malnourished).
Notes: An interesting aspect of the absorption of ingested lead is how it can vary depending upon metabolic status. A well fed adult might absorb 6% of an ingested lead dose; a fasting adult might absorb more. Children, even when well fed, may absorb 30% of a lead dose, and still more when iron deficient. Pregnant women are also likely to absorb lead more efficiently. Children and pregnant women are supporting bone development. Lead is more likely to be absorbed when the gut is “primed” to absorb Fe and Ca.

## Slide 7
Notes: Children at Risk
Children ages 9 months to 2 or 3 years old are most at risk because they crawl on the floor, breathe in a zone nearest the floor, get lead on their hands during floor contact activities, and engage in hand-mouth activities most commonly. This age group at highest risk for lead poisoning, is targeted in recommended childhood surveillance policies.
The effects of childhood lead poisoning are not equally distributed in the U.S. (or any) society. Childhood lead poisoning is more common in inner cities, among the poor, and among African Americans.

## Slide 8: How Does Lead Enter the Body?
3. Skin
Skin is relatively impervious to lead, lead oxides , or lead salts. Some may get through scrapes or wounds, but organic leads (such as in leaded gasoline), will go through skin into the bloodstream quite well.
Notes: There is a third route of entry. Lead, lead salts, and lead oxides do not penetrate intact skin. Organic lead is different. Like many organic metals, alkyl leads are readily absorbed through the skin. In addition, they are taken up into organs more rapidly. They are very dangerous.

## Slide 9: Does the Route of Entry Matter?
Lead, lead salts, lead oxide, all have same toxicity (whether inhaled or ingested), but more is absorbed when inhaled.
Organic lead has greater affinity for CNS – therefore skin absorption may be SERIOUS
Notes: Organic Lead
Lead is dangerous regardless of the route of entry. Organic lead has the greatest CNS toxicity. Because only organic lead is absorbed through the skin, you might say that the dermal route of entry has particular dangers. Similarly, an ingested dose is less fully absorbed than an inhaled exposure.

## Slide 10: Where does lead go once in the body?
  Lead is absorbed into the bloodstream rapidly.
  It then travels to “soft tissue” such as kidneys, lungs, brain, spleen, muscles, and heart. This occurs within a matter of days
  After several weeks, most lead which is not excreted by urine (primary route), feces, or exocrine secretions (including breast milk) moves into the long term storage area, bones (and teeth).
Notes: Lead Metabolism (Uptake and Distribution)
Lead is rapidly absorbed into the bloodstream via any route of entry. Some is incorporated into the building of hemoglobin molecules in red cells. We will discuss that more when we get to how lead causes anemia. Next, lead travels to “soft tissues” such as kidneys, lungs, brain, spleen, muscles, and heart. This occurs within a matter of days. Blood lead level peaks in the several days following exposure. The half life of lead in blood is approximately equivalent to the half life of the red cell; (thought question for students – why is this so?) around one month. After that, most lead which is not excreted by urine (primary route), feces, or exocrine secretions (including breast milk) moves into the long term storage area, bones (and teeth). About 94% of an average adult’s total lead burden (the total amount of lead in all tissues throughout the body) is in bones and teeth. In children, this is about 73%.
Lead is also found in hair. If one is very careful to wash the exterior hair surface, it is possible to “time” the deposition of lead in hair. This requires exquisite attention to laboratory procedures.

## Slide 11: Where does lead go once in the body?
    About 94% of adults total lead burden is in bones and teeth
    Only about 73% for children
  4. Lead in bones and teeth equilibrates over time and
  circumstance with other “compartments”.
  Some lead is also found in hair.
Notes: Lead Metabolism (Uptake and Distribution)
Lead is rapidly absorbed into the bloodstream via any route of entry. Some is incorporated into the building of hemoglobin molecules in red cells. We will discuss that more when we get to how lead causes anemia. Next, lead travels to “soft tissues” such as kidneys, lungs, brain, spleen, muscles, and heart. This occurs within a matter of days. Blood lead level peaks in the several days following exposure. The half life of lead in blood is approximately equivalent to the half life of the red cell; (thought question for students – why is this so?) around one month. After that, most lead which is not excreted by urine (primary route), feces, or exocrine secretions (including breast milk) moves into the long term storage area, bones (and teeth). About 94% of an average adult’s total lead burden (the total amount of lead in all tissues throughout the body) is in bones and teeth. In children, this is about 73%.
Lead is also found in hair. If one is very careful to wash the exterior hair surface, it is possible to “time” the deposition of lead in hair. This requires exquisite attention to laboratory procedures.

## Slide 12: How Does Lead Get Out of the Body
Kidneys- urine
Bowels- stool
Glands- sweat
Breast- breast milk
Hair, nails, teeth (very slow turnover)
It takes >10 years to turn over one half the body’s stored lead. Bone source slowly leaches into the blood.
Notes: Lead Excretion, Implications for Breast Feeding
While the half life of lead in the adult red cell is on the order of 30 days, it is decades in bone. Lead is excreted from the body by various routes, principally in urine, but also in secretions such as breast milk. This implies that nursing mothers who have been lead poisoned even in the remote past, may need to get their breast milk tested. (This has implications for women who are or plan to be pregnant if they have a high body burden of Pb).

## Slide 13: What Does Lead Do?
Lead inhibits certain types of enzymes,
Particularly enzymes dependant upon
sulfhydryl groups.
Organ systems affected include:
Neurologic Endocrine
Reproductive Musculoskeletal
Blood Renal
GI
Notes: What does Lead Do In The Body?
Once distributed to organs, lead inhibits certain types of enzymes by binding to sulfhydryl groups. The results are protean, affecting many organ systems. Interference with the synthesis of heme in the red cell is an illustrative example. There is also competition with calcium in several systems including mitochondrial (cellular) respiration and degradation of various nerve cell functions. Lead also affects RNA and DNA, although mechanisms are not clear.

## Slide 14: What Does Lead Do?
Interference with the synthesis of heme in the red cell .
There is also competition with calcium in several systems including mitochondrial (cellular) respiration and degradation of various nerve cell functions.
Lead also affects RNA and DNA, although mechanisms are not clear.
Notes: What does Lead Do In The Body?
Once distributed to organs, lead inhibits certain types of enzymes by binding to sulfhydryl groups. The results are protean, affecting many organ systems. Interference with the synthesis of heme in the red cell is an illustrative example. There is also competition with calcium in several systems including mitochondrial (cellular) respiration and degradation of various nerve cell functions. Lead also affects RNA and DNA, although mechanisms are not clear.

## Slide 15: Microcytic Anemia with Basophilic Stippling
Larger area is a thick thick smear to demonstrate the frequency of basophilic stippling
Notes: Lead and The Red Cell:
Microcytic Anemia with Basophilic Stippling
Inhibition of the enzymes that are involved in the formation of the hemoglobin molecule can be detected at BLLs as low as 10 μg/dL whole blood, and intermediate products of inhibited hemoglobin formation (i.e. protoporphyrins) begin to appear at slightly higher levels. While we might expect that detection of protoporphyrins would be an effective test for lead poisoning, its usefulness is limited, as we will see below.
These incomplete hemoglobin molecules break down and are scavenged along with the red blood cells containing them. The accelerated scavenging of cells leads to anemia, initially normochromic and eventually a microcytic, hypochromic anemia with iron deficiency. As lower iron levels also promote increased uptake of lead from the gut, this sets up a “positive feedback loop” for lead poisoning and iron deficiency – each promoting the other. Children have better compensatory erythropoieten responses than adults, and may delay onset of anemia.
The broken down molecules accumulate and stain with a basophilic stain. This slide shows the classic microcytic anemia with basophilic stippling of lead poisoning. This picture should be rare! Good hygiene should prevent, and good surveillance will pick up, lead poisoning before it reaches this stage.
Eosinophilia is also seen in some cases of lead poisoning.

## Slide 16: HEALTH HAZARDS
Lead interferes with the formation of the hemoglobin in blood and
will cause anemia.
Lead causes cellular
kidney damage which
leads to kidney failure.
It can cause reduced sperm count
and decreased fertility.
HEMOGLOBIN
ANEMIA DECREASE
FERTILITY
KIDNEY DAMAGE

## Slide 17: Health Hazards cont'd
Lead can damage the nervous system, the blood forming organs, kidneys, and reproductive system.
Chronic exposure initially
damages the blood forming
and reproductive organs, and
eventually cause peripheral nerve
and central nervous system damage.
Lead can pass from mother
to infant through the
placenta.
NERVOUS
SYSTEM
BLOOD
FORMING
ORGANS
CENTRAL
NERVOUS
SYSTEM
REPRODUCTIVE
ORGANS

## Slide 18: Lead and Adult Reproduction
Reproductive
Females
- Miscarriage, still birth
- Inability to conceive
- premature births
Males
- Decreased libido
- impotence
- Decreased sperm motility
- Sperm abnormalities: counts, abnormal forms
Notes: Lead and Adult Reproduction
Lead diminishes fertility in exposed men and women, even beyond the well-recognized outcomes of spontaneous abortion and stillbirth in heavily exposed mothers. Additional outcomes in exposed males are diminished libido, decreased sperm production, and decreased sperm motility.
A famous U.S. Supreme Court Decision illustrates some of the complex social issues surrounding the use of reproductive toxins. Johnson Controls, a manufacturer, recognized the liability in exposure of pregnant (or even non pregnant but fertile female) workers. Their approach to mitigating the danger was to make medical certification of sterility a job requirement among reproductive age women. This requirement was contested up to the U.S. Supreme Court where it was found to violate basic constitutional rights (and incidentally did nothing to prevent exposures, including exposures to men whose reproductive systems were also at risk). An outcome of this decision is that material substitution, industrial engineering, and personal protection are still preferred workplace approaches to preventing lead poisoning, regardless of gender or reproductive status.

## Slide 19: Lead and the Kidney Acute and Chronic Disease
Lead nephropathy (Fanconi syndrome) is characterized by dysfunction of proximal tubules (aminoacidura, glucosuria, phosphaturia with increased sodium excretion, and deceased uric acid excretion.
Chronic kidney disease may also arise, sometimes associated with gout.
Notes: Lead and the kidney
Lead is a cause of both acute and chronic renal disease. Acute nephropathy has been more clearly described, and fortunately it is becoming much rarer. Acute nephropathy is characterized by dysfunction of proximal tubules (Fanconi’s syndrome), manifested as aminoaciduria, glucosuria, phosphaturia with hypophosphatemia, and increased sodium excretion with decreased uric acid excretion. These effects are considered to be largely reversible. The risk of renal damage goes up during chelation treatment, which may present substantial quantities of lead to the tubules in a short time.
The nature of chronic nephrotoxicity is less clear, and seems to be characterized by chronic interstitial and peritubular fibrosis. In addition; the gout associated with lead poisoning (“saturnine gout”) is both an effect of altered uric acid excretion and a potential cause of chronic kidney damage.

## Slide 20: Key Presenting Symptoms
Mild | Moderate | Severe
Fatigue | Paresthesia | Paralysis
Irritability | Myalgia | Colic
 | Arthralgia | 
 | Headache | 
 | Tremor | 
 | GI Distress | 
Notes: Symptoms
Most lead poisoned children are not described by their parents as having symptoms. Most adults present with subtle symptoms, such as irritability, rather than some of the more dramatic symptoms listed on this slide.

## Slide 21: Physical Findings
Early Chronic
Wrist Drop Transverse Nail Lines
Distal Sensation Blue-Black Gum Lines
foot weakness
diminished distal vibration sensation
these findings signifies failure of workplace or environmental protection
Notes: Physical Findings
Physical findings are usually absent, unless lead poisoning is advanced. A modest goal of hygiene and surveillance policy is to insure that physical findings are rare! Nevertheless, there are a number of physical findings that should be sought: wrist and foot weakness, diminished distal vibration sensation and propioception. Historically important but rarely seen physical findings include transverse furrows on the nails due to nail growth arrest in severe lead poisoning, and a blue-black discoloration of the gum (“lead line”) due to lead sulfide metabolism by sulfide-loving bacteria. The presence of these findings signifies entrenched failure of workplace or environmental protection.

## Slide 22: Permissible Exposure Limits
The permissible exposure limit (PEL) for
an 8 hour time weighted average
(TWA) exposure to airborne lead is 50 micrograms per cubic meter (g/m3)
of air.

## Slide 23: General Workplace Control Practices
Use reduced lead paint coatings
Only low lead content paint shall be used in the interior of residential structures or on other surfaces which may pose an ingestion hazard.

## Slide 24: VENTILATION
To the extent feasible, fixed local exhaust ventilation
connected to filters or other collection systems,
approved by the industrial hygienist, shall be
provided at the point of airborne particulate generation.

## Slide 25: VENTILATION cont'd
The ventilation systems shall be
tested every 3 months and with 5
days of any change which may result
in a change of employee exposure.

## Slide 26: Personal Protective Equipment
Personnel involved in work where the concentration of lead exceeds
the PEL or the possibility of eye or skin irritation exists, shall remove the clothing worn to and use protective clothing.

## Slide 27: Personal Protective Equipment cont'd
Full body, one piece coveralls supplied and laundered
by the employer or a contractor shall be used. Clothing
shall be waterproof when wet lead is handled.
Durable gloves and head coverings shall be used.

## Slide 28: Personal Protective Equipment cont'd
Slip resistant shoe covers or lightweight rubber boots shall be provided. Disposable shoe covers may also be used.
Face shield, vented goggles, or other appropriate protective equipment shall be provided and used whenever the possibility of eye irritation exists.
Clean protective clothing shall be provided at lease weekly, or daily when the 8 hr TWA concentration exceeds 200 micrograms.

## Slide 29: Warning Signs
gns shall be provided and displayed at each
location where airborne lead may exceed the PEL.
The warning sign may contain a listing of required
protective equipment.
DANGER
Lead Work Area
Poison
No Smoking, Eating, or Drinking

## Slide 30: LUNCHROOMS
Lunchrooms shall be provided for employees who work in areas where the airborne lead exposure is above the PEL.
These lunchrooms shall have a positive
pressure, filtered air supply and be readily accessible.
Protective clothing and equipment shall be
removed prior to entering the lunchroom.

## Slide 31: LUNCHROOMS cont'd
In lead work areas, the following shall be prohibited:
Eating
Drinking
Chewing or smoking tobacco
Applying makeup
Storage of food or tobacco
All lead workers shall wash their hands and face
prior to eating, drinking, smoking, or applying
cosmetics.

## Slide 32
Medical Surveillance and Workplace Removal in Adult Workers
Medical surveillance is triggered by air monitoring results (or other knowledge of exposure).
In addition to venous blood leads, an Erythrocyte protoporphyrin or zinc protoporphyrin ( ZPP)
creatinine, BUN and CBC should be obtained at baseline and whenever there is a medical rationale for repeat testing.
Notes: Medical Surveillance and Workplace Removal in Adult Workers
Possibly because lead work is often performed in small and even marginal businesses, a minority of lead-exposed employees actually receive OSHA-mandated medical surveillance for the early detection
of lead poisoning. There are 2 differing OSHA surveillance strategies - the one for construction workers is more generally useful.
Medical surveillance is triggered by air monitoring results (or other knowledge of exposure). It should be noted that additional workers who might be exposed can prudently be put in the program. It is generally easier and safer for employers to be inclusive than exclusive.
In addition to venous blood leads, an EP (or ZPP), creatinine, BUN and CBC should be obtained at baseline and whenever there is a medical rationale for repeat testing.

## Slide 33: Adult Return to Work
Lead poisoned workers can return to the workplace when blood lead is <40 µg/dl.
Symptomatic workers can remain out of the workplace at lower levels.
Workers whose blood lead is near 40 µg/dl are most likely to be able to remain in the workplace if they can perform modified duty without lead exposure.
Notes: Workplace Removal and Return to Work
Construction Site Inspections are triggered by BLLs>40 μg/dl. Workers should be removed when the blood lead is >50μg/dl, and an OSHA log entry is made. In addition, return to work at 40 μg/dl is a very narrow window of “protection”, and recurrent levels above 50 μg/dl are quite possible with only small additional lead exposure once the worker returns. Finding jobs without lead exposure for recently poisoned workers enhances the chance that they can both return and stay in the workplace.
[ OSHA 1926. 62 - http://www.osha-slc.gov/OshDoc/DIRECTIVE_data/CPL_2.2_58.html ]

## Slide 34: The Key to “Treatment” of Lead Poisoning
Remove from exposure, or otherwise prevent
exposure.
Workplace
Substitution
Engineering
Personal Protection
Job Placement
Notes: Treatment of Lead Poisoning
In a moment, we will describe medical approaches to treatment. None of the drugs have a meaningful chance to help victims who are still exposed, and they may even worsen the severity of illness if exposure persists. So, the real key to treatment is to engineer the home or workplace, or change the living conditions or job of the victim.

## Slide 35
Treatment of Lead Poisoning-Chelation
Chelation is an adjunct to the real treatment in lead poisoning. For children and adults, the real treatment is to decrease exposure. What chelation can do is speed up the process of reducing the lead in circulating blood. Chelation is much less effective at attacking bone stores; a single chelation treatment (for example 5 days of I.V. EDTA) mobilizes much less than 10% of whole body lead burden.
Notes: Treatment of Lead Poisoning-Chelation
Chelation is an adjunct to the real treatment in lead poisoning. For children and adults, the real treatment is to decrease exposure. What chelation can do is speed up the process of reducing the lead in circulating blood. Chelation is much less effective at attacking bone stores; a single chelation treatment (for example 5 days of I.V. EDTA) mobilizes much less than 10% of whole body lead burden.
The reason to chelate are to reduce symptoms or physical findings, or because there is legitimate fear of untoward outcomes (such as seizure). The advantages of a quick drop in circulatory blood lead must be weighed against possible complications of chelation such as kidney damage or arrhythmia or even increased blood lead if exposure persists. In addition, the quick decrease in circulating stores is not permanent. The equilibration between “compartments” explains the “bounce back” (increase in blood lead levels) that commonly follows treatment.
Until recently, it was common to chelate symptomatic children whose blood lead was 20-45 µg/dl, in an effort to preserve and protect CNS function. A recent controlled therapeutic trial found no detectable benefit of this practice in children 1-3 years old with blood lead levels of 20-44 µg/dl. When followed to grade school, children treated with chelation did not perform better than untreated, lead-poisoned peers. (Rogan WJ et al. The effect of chelation therapy with succimer on neuropsychologic development in children exposed to lead. N Engl J Med 2001; 344: 1421-6).

## Slide 36: Prevention of Lead Poisoning
Prevention of lead poisoning is a superior public health measure; medical treatment alone is disappointing.
The key to treatment is cessation of exposure, and the public health need is to consider and find other possible victims.
Notes: The long-term success of our efforts to prevent lead poisoning will ultimately correlate with the amount and availability of lead in the home and work environment.
We have taken some effective primary prevention measures, such as removing lead from gasoline and virtually all points. Where lead is already in the home environment, we have relied on secondary prevention measures such as medical surveillance, rather than taking the expensive primary route of attacking the presence of lead by removal. This strategy has been partially effective, and is likely to remain partially effective. Thus, a high degree of alertness and ongoing medical surveillance strategies are needed to diminish the negative outcomes of lead exposure in our children. In this one situation, we must survey our children as carefully as we normally survey more discrete populations of adult workers.
For adult workers, industrial hygiene and medical surveillance have worked well in larger, safety conscious organizations. Many businesses working with lead are small or operate at the economic margins. Lead poisoning
persists, and is often detected only after the fact, in these work environments.

## Slide 37
some effective primary prevention measures, such as removing lead from gasoline.
Where lead is already in the environment, we have relied on secondary prevention measures such as medical surveillance, rather than taking the expensive primary route of attacking the presence of lead by removal. This strategy has been partially effective.
Notes: The long-term success of our efforts to prevent lead poisoning will ultimately correlate with the amount and availability of lead in the home and work environment.
We have taken some effective primary prevention measures, such as removing lead from gasoline and virtually all points. Where lead is already in the home environment, we have relied on secondary prevention measures such as medical surveillance, rather than taking the expensive primary route of attacking the presence of lead by removal. This strategy has been partially effective, and is likely to remain partially effective. Thus, a high degree of alertness and ongoing medical surveillance strategies are needed to diminish the negative outcomes of lead exposure in our children. In this one situation, we must survey our children as carefully as we normally survey more discrete populations of adult workers.
For adult workers, industrial hygiene and medical surveillance have worked well in larger, safety conscious organizations. Many businesses working with lead are small or operate at the economic margins. Lead poisoning
persists, and is often detected only after the fact, in these work environments.

## Slide 38: Sources of Lead- Air
Uncontaminated Contaminated
1-2 μg/m3 4-16 μg/m3
Near Smelter
Notes: Sources in Air
Significant amounts of lead can be in the air under certain circumstances. “Uncontaminated” air has, at most, 1-2μg/m³ of lead. This goes up a little downwind of coal burning power plants. The outdoor air near a smelter can be substantially contaminated and may have 16μg/m³ of lead. In occupational environments, such as within bridge repair spaces, the air contamination may be so extensive as to cause lead poisoning in a very short time. A worker misusing a respirator for a matter of minutes may become poisoned, with blood lead well above 40 µg /dl.
Other trades with significant respiratory exposure include house painting, rifle range instruction, battery or ammunition production or reclamation, junk yard work and “ship breaking”.

## Slide 39: SOURCES OF LEAD- Water
Uncontaminated
Standards vary Internationally.
In U.S. <15 μg/L 99% of water supplies
When there is contaminated water in a home, it is most often from some source other than a generally contaminated municipal water supply. Leached lead from old lead pipes are more common problems at the level of individual homes
Notes: Lead Ingested in Water
Lead may be ingested in water. About 70% of the population lead burden is estimated to come from water, although water is generally less important in actual poisoning. All humans carry some chronic lead stores which add to the total lead burden in society. This burden is always undesirable, yet only a minority of us become lead poisoned. Standards for uncontaminated water vary from country to country. The action level for lead in U.S. water is 15ppb since 1991. The majority of municipal sources are compliant. This improvement over the1962 Public Health Service Standards of 50ppb, reflecting increased public health vigilance over time. When there is contaminated water in a home, it is most often from some source other than a generally contaminated municipal water supply. Leached lead from old lead pipes or from lead-soldered plumbing joints are more common problems at the level of individual homes. Lead used as a plasticizer in long hose lines is also a potential source in “impromptu” water supplies.