## Slide 1: Powder density
Lab4 Industrial pharmacy

## Slide 2: Powder bulk density
It is simply expresses the amount (usually weight or mass) of a powder in a specified volume.

## Slide 3: Composition of powders and there relation with volume
Powders are composed of: particles and voids.
The volume occupied by a given number of particles depends on how closely they are packed.
The packing of particles depends on:
A- shape
B- cohesiveness
C- short-range motion
D- external forces.

## Slide 4: Tapped density
Describe the bulk-density of a powder (or granules) after consolidation/compression ("tapping“) the container of powder a measured number of times, usually from a predetermined height.
The method of "tapping" is best described as lifting and dropping.

## Slide 5: Measuring Bulk density
Tapped density measured by tapping graduated glass measuring cylinder manually or by mechanical device.
(the total capacity of the cylinder to be used, and the readability of its scale are stated).
Is determined by pouring pre-sieved bulk drug into a graduated cylinder via a large funnel and measuring the volume and weight.
Measuring tapped density

## Slide 6: Types of tapping: 1. Manual tapping 2. Mechanical tapping
1. Manual tapping:
The raising and lowering of the cylinder by hand is done either without reference to the height traversed and arbitrary acceleration in both upward and downward directions; the hand remaining in contact with the cylinder at all times (hand tapping).
(The cylinder containing the powder is tapped by repeatedly striking its base down onto a hard surface).

## Slide 7: 2. Mechanical tapping
Tap density analyzers (tap density testers) Use an electric motor to turn a cam under a specially constructed cylinder holder. The holder secures the cylinder to a vertical shaft which runs in a low friction bearing.
The tapping rate is expressed in taps per minute; the rate being typically a few hundred.
The actual rate is determined by the rotational speed of the cam under the shaft/platform.

## Slide 8
Digital or electromechanical counters are usually incorporated in the device to automatically stop the cam rotation after a predetermined (yet adjustable) number of taps.
The height through which the container falls is (drop height or stroke). It is set by the distance between the highest point on the cam and the striking surface.

## Slide 9: How to correct the density problem:
Milling
Slugging
Formulation

## Slide 10: Benefits of bulk density:
Important in the consideration the size of high dose capsule product.
The homogeneity of a low dose formulation in which there are large differences in drug and excipient densities.
knowing the dose and formulation density to determine the appropriate size for a capsule formulation.

## Slide 11: Tapped density and powder flowability
The change in tapped powder volume (related to flow properties of powders)
It can be determined by compressibility which is computed from powder density using the following equation:
% compressibility =× 100
𝜌t- tapped density
𝜌o- bulk density

## Slide 12
% compressibility | Flowability
5-15 | Excellent
12-16 | Good
18-21 | Fair passable
23-35 | Poor
33-38 | Very poor
More than 40 | Very very poor