## Slide 1: In vitro dissolution study of per – oral tablet
Assistant Prof. Anas Tariq
Lec. Nora Zawar
Lec. Zeina Dawood
Lec. Sura Zuhair

## Slide 2: Introduction :
Dissolution is a process of going into solution form .
A basic principle of drug absorption is that absorption takes place only after a drug is in solution.
this means that drug given orally in solid dosage form must dissolve in GIT fluid before absorption occurs

## Slide 4
DISSOLUTION RATE : Is DEFINED AS THE AMOUNT OF SOLID SUBTANCE THAT goes into solution per unit time under standard condition of temperature , Ph and solvent composition
Dissolution is the rate limiting step for hydrophobic poorly soluble drug for example, griseofulvin and spironolactone

## Slide 6: Expression of solubility

## Slide 7
BCS Class | Solubility | Permeability | Examples of Drugs | Formulation / Bioavailability Considerations
Class I | High | High | Metoprolol, Propranolol, Verapamil, Acetaminophen | Usually good oral absorption; dissolution is rate-limiting. Standard immediate-release (IR) formulations are suitable.
Class II | Low | High | Ketoconazole, Danazol, Carbamazepine, Ibuprofen | Dissolution is the limiting step. Use solubility enhancement techniques (e.g., nanoparticles, solid dispersions, surfactants).
Class III | High | Low | Metformin, Cimetidine, Atenolol, Ranitidine | Permeability is rate-limiting. Formulation focuses on permeability enhancers or transporter considerations.
Class IV | Low | Low | Hydrochlorothiazide, Furosemide, Paclitaxel | Poor oral bioavailability; requires special delivery systems (nanofibers, nanoparticles, lipid carriers).
BCS CLASSIFICATION

## Slide 8: TYPES OF DISSOLUTION APPARTUS

## Slide 9: What is sink condition?

## Slide 10
Dissolution tests can be conducted in simple buffer solutions or in more bio-relevant dissolution media
Dissolution tests are normally performed under sink conditions
Sink condition is the ability of the dissolution media to dissolve at least 3 times the amount of drug that is in your dosage form.
Having sink conditions helps your dissolution have more robustness as well as being more biologically relevant.

## Slide 11
Procedure ( Dissolution study of nitrofurantoin tablets)
Fill the jars with 1 L of dissolution fluid (artificial gastric juice)
Put the jars in a thermostatically controlled water bath at 37 (switch water bath on)
Place 1 tablet of nitrofurantoin in the dissolution apparatus (paddle type).
Set the speed on 50 r.p.m
Withdraw 5 ml each 10 min for 50 minutes

## Slide 12
Substitute for the volume withdrawn each time interval using a fresh (artificial gastric juice) previously maintained at 37º C
Analyze samples of nitrofurantoin by reading the
absorbance on a UV spectrophotometric at 370 nm.
Use the straight line equationy=0.0036+0.07x to
obtain the concentration of the dilutions.
Note : the conc. Is in mcg/ml

## Slide 13
1-Con.(mcg/ml)X vol. of dissolution media =(mcg amount of drug released into the dissolution media then convert it to mg
2- multiply the amount with dilution factor (if you made dilution )
3-% of drug released = amount of drug release /amount of drug in the tablet *100
4- then put the time column and percent of drug release column together then click insert, scatter with smooth lines and markers

## Slide 15
120
100
80
60
40
20
0
0
10
20
30 40
time in minutes
50
60
70
percent of drug release
Chart Title