## Slide 1: Parasitology Lab Fecal Examination
• Introduction to fecal examination
• Specimen collection and preservation
• Examination methods

## Slide 2: Specimen Collection
• Collect stool in clean, dry, leak-proof container
• Avoid contamination with urine or water
• Examine fresh stool immediately or preserve properly

## Slide 3: Preservation of Stool Specimens
• Preserve as soon as possible
• Use 10% formalin if kits are unavailable
• Stool : preservative ratio = 1 : 3
• Mix well, especially formed stool

## Slide 4: Staining Methods
Temporary stains:
• Saline
• Iodine
• Eosin
Permanent stains:
• Iron hematoxylin
• Trichrome stain

## Slide 5: Fecal Examination
Macroscopic examination:
• Color and consistency
• Blood or mucus
• Proglottids or adult worms
Microscopic examination:
• Wet mount
• Concentration methods

## Slide 6: Concentration Methods
Used to increase detection of parasites
• Sedimentation methods
• Flotation methods

## Slide 7: Sedimentation Method
• Based on parasites being heavier than debris
• Parasite eggs and cysts settle at the bottom
• Example: Formalin–ether sedimentation
• Effective for heavy eggs (e.g. trematodes)

## Slide 8: Formalin-Ether Sedimentation – Steps
1. Mix stool sample with formalin
2. Strain the mixture
3. Add ether
4. Centrifuge the sample
5. Discard supernatant
6. Examine sediment under microscope

## Slide 10: Flotation Method
• Based on difference in specific gravity
• Parasites float to surface in flotation solution
• Example: Zinc sulfate flotation , Saturated Salt Flotation – Steps , Baermann Technique – Steps
• Useful for protozoan cysts and light eggs

## Slide 11: Zinc Sulfate Flotation – Steps
1. Mix stool with zinc sulfate solution
2. Strain the suspension
3. Centrifuge
4. Add more solution to form meniscus
5. Place coverslip
6. Examine microscopically

## Slide 13: Sedimentation vs Flotation
Sedimentation:
• Good for heavy eggs
• High sensitivity
Flotation:
• Good for light eggs and cysts
• Cleaner background