## Slide 1
Characteristics of Logic Families : I-V Requirements
Voltage and Current parameters:
VIH (max)
VIH {
VIH (min)
VIL(max)
VIL{
VIL(min)
Fig.1 (a) Input logic levels
VOH (max)
VOH {
VOH (min)
VOL(max)
VOL{
VOL(min)
Fig.1 (b) Output logic levels
VIH -High-Level Input Voltage:
It is the range of voltage in a gate for the input to be treated as logic 1
Range = VIH(max) - VIH(min)
VIL(max) -Low-Level Input Voltage:
It is the range of voltage in a gate for the input to be treated as logic 0
Range = VIL(max) - VIL(min)
VOH -High-Level Output Voltage:
It is the range of voltage in a gate for the output to be treated as logic 1
Range = VOH(max) – VOH(min)
logic 1
logic 0
Intermediate
Level
logic 1
logic 0
Intermediate
Level

## Slide 2
VOL- Low Level Output Voltage:
It is the range of voltage in a gate for the output to be treated as logic 0
Range = VOL(max) – VOL(min)
range (logic1) is
IIH - High Level Input Current:
It is the current that flows in the input when voltage of VIH
applied.
range (logic0) is
IIL- Low Level Input Current:
It is the current that flows in the input when voltage of VIH
applied.
range (logic1)
IOH - High Level Output Current:
It is the current that flows from in the output when voltage of VOH
is obtained under given load.
range (logic0)
IOL- Low Level Output Current:
It is the current that flows from in the output when voltage of VOL
is obtained under given load.
Fig.2: Currents and voltages in the two logic states

## Slide 3
Fan-in and Fan-out:
Fan-in: the number of inputs of a gate that it can handle without impairing its normal operation.
1
2
3
Fan-in = number of inputs
Propagation delay increases with number of inputs. Therefore a 2 input NAND gate is faster than 4 input NAND gate.
Fan-out: The number of standard loads can be connected to the output of the gate without affecting its normal operation. Sometimes the term loading is used.
Fig.3: fan-out computation
130

## Slide 4
IIH
Low state fan-out = IOL (max)
IIL
For TTL gate:
40µ𝐴
High state fan-out = 400µ𝐴 = 10
1.6mA
Low state fan-out = 16mA = 10
Noise margin:
-The unwanted signals are referred to as noise.
- Noise margin is the maximum noise added to an input signal of a digital circuit that does not cause an undesirable change in the circuit output.
Fig.4: Noise margins
131
Fan  out  min( IOH , IOL )
I IH I IL
High state fan-out = IOH (max)

## Slide 5
2
P PHL
132
PLH
t = 1 (t + t )
Figure 5 shows logic gates with different fan-outs and their corresponding propagation delays.
High state noise margin:
V = V (min) – V (min)
NH OH IH
Low state noise margin:
V = V (max) – V (max)
NL IL OL
Propagation delay:
The average transition-delay time for the signal to propagate from input to output when the binary signal changes in value
tPLH : It is the delay time measured when output is changing from logic 0 to logic 1 state (LOW to HIGH).
tPHL: It is the delay time measured when output is changing from logic 1 to logic 0 state (HIGH to LOW).
When tPHL and tPLH are not equal, the larger value is considered as a propagation delay time for that logic gate, i.e.
tp = max (tPLH, tPHL)
Sometimes propagation delay tp is taken to be the simple average of the two :

## Slide 6
Fig.5: Fan-outs and corresponding propagation delays
Fig.6: Currents lCCH and ICCL
CC
Power dissipation:
-The power needed by the gate is expressed in mW.
ICCL
PD (avg)  ICC (avg) VCC
2
I (avg)  ICCH
133

## Slide 7
Example 2: A certain gate draws 1.8 mA when its output is HIGH and 3.2 mA when its output is LOW. What is its average power dissipation if VCC is 5 V and it is operated on a 50 % duty cycle?
Solution: The average Ice is given as,
I
CC(avg)
= ICCH+ICCL
2
=
= 2.5 mA
Then average power dissipation is given as, PD (avg) = ICC(avg) X VCC = 2.5 mA x 5 V = 12.5 mW
Speed-power product(J)=Propagation delay (Seconds) x Power dissipation
(joules/seconds)
Example 3: For a certain IC family, propagation delay is 10 ns with an average power dissipation of 6 mW. What is its speed power product?
Solution: The speed- power product is given as,
SPP = Propagation delay x Average power dissipation
= 10 ns x 6 mW x 60 pico joules (pJ)
Example 4:
If V cc = 5VCC= 5V, ICC (0) 22 mA, 1CC (1) = 8mA, VOH = 2.4 V, VIH =2 V,
VOL = 0.45 V, VIL = 0.8 V, tPHL = 15nsec, tPLH = 22 nsec, IIH = 40𝜇A, IOH = 5.2 mA.
calculate :
Noise margin logic 1 and logic 0.
Power dissipation.
Propagation delay and figure of merit.
Fan-out.

## Slide 8
Solution:
i) Noise margin logic 1
VNH = VOH(min) - VIH(min)
= 2.4 V — 2 V
Noise margin logic 0
VNL = VIL(max) — VOL(max)
= 0.8 V — 0.45 V
ii) Power dissipation
ICC(avg) XVCC
I
CC(avg)
𝐼𝐶(0)+𝐼𝐶𝐶(1)
=
2
= 15 mA
∴ Power dissipation = 15 mA x5 V
= 75 mwatts
iii) Propagation delay
tp = max (tPLH tPHL)
tp = tPGL = 22nsec
2
p PLH PHL
t = 1 (t t )
= 1 (22+15)nsec
2
= 18.5nsec
Figure of merit = SPP = Delay x Power dissipation
=18.5 nsec x 75 mwat
=1387.5 pico joule
iv)Fan-out =
IOH(max)
IIH(MAX)
= 5.2mA = 130
40μA
VNH = 0.4 V
VNL = 0.35 V