## Slide 1: 2CREEP
الجامعة المستنصرية
كلية الهندسة – قسم الهندسة الميكانيكية
مادة مواد هندسية
د. ناظم مجبل فالح

## Slide 2: Creep test
Consist of subjecting a specimen to a constant tensile load at a certain temp.
And measure the changes in length at various time increments.
A typical creep curve usually consist of primary, secondary and tertiary stage (refer Fig below).

## Slide 3
The specimen fails by necking and fracture called rupture or creep rupture.
The creep increase with;
    Temp
    Applied load

## Slide 4: Important of creep
Design against creep usually involve knowledge of the secondary (linear) range and its slope.
The creep rate can be determined reliably only when the curve has a constant slope.
Generally, resistance to creep increase with the melting temp of a material.
Stainless steel, superalloys, refractory metals and alloys are commonly used in applications where resistance to creep is required.

## Slide 5: Stress relaxation
Closely related to creep.
The stress resulting from a loading of structural component decrease in magnitude over a period of time even though the dimensions of the component remains constant.
Example;
  the decrease of tensile stress of a wire in tension between 2 fixed ends
  Rivets, bolts, guy wires and similar parts under tension, compression or flexure.