## Slide 1
Moment of a Force
When a force is applied to a body it will produce a tendency for the body to rotate about a point that is not on the line of action of the force. This tendency to rotate is sometimes called a torque, but most often it is called the moment of a force or simply the moment.
The magnitude of the moment is directly proportional to the magnitude of F and the perpendicular distance or moment arm d.
Direction. The direction of Mo is defined by its moment axis, which is perpendicular to the plane that contains the force F and its moment arm d. The right-hand rule is used to establish the sense of direction of Mo. Since in this case the moment will tend to cause a counterclockwise rotation, the moment vector is actually directed out of the page.
Magnitude. The magnitude of is Mo
Lecture 4

## Slide 2
Resultant Moment.
For two-dimensional problems, where all the forces lie within the x–y plane, Fig. below, the resultant moment (MR)O about point O (the z axis) can be determined by finding the algebraic sum of the moments caused by all the forces in the system. As a convention, we will generally consider positive moments as counterclockwise since they are directed along the positive z axis (out of the page). Clockwise moments will be negative.
Important Points
● The moment of a force creates the tendency of a body to turn
about an axis passing through a specific point O.
● Using the right-hand rule, the sense of rotation is indicated by the
curl of the fingers, and the thumb is directed along the moment
axis, or line of action of the moment.
● The magnitude of the moment is determined from MO = Fd, where d is called the moment arm, which represents the perpendicular or shortest distance from point O to the line of action of the force.
● The principle of moments states that the moment of a force about a point is equal to the sum of the moments of the force’s components about the point. This is a very convenient method to use in two dimensions.

## Slide 3
EXAMPLE: Determine the moment of the force in Fig. a below about point O.
SOLUTION
The x and y components of the force are indicated in Fig.b. Considering counterclockwise moments as positive, and applying the principle of moments, we have
+ MO = - Fxdy - Fydx
= -(5 cos 45° kN)(3 sin 30° m )- (5 sin 45° kN)(3 cos 30° m)
= -14.5 kN.m = 14.5 kN.m